## Slide 1: Implementation of Scheduling Algorithms to Accelerate Robotic Applications
Andreas Andreou
Institute of Computer Engineering/ Chair of Adaptive Systems

## Slide 2: Objective
RTL-Implementation of Scheduling Algorithms
Internal Characteristics
Generalizability
Scalability
Feasibility
Performance

## Slide 3: State-of-the Art Scheduling Algorithms
Fixed Priority
Non-Pre-emptive
Pre-emptive
Earliest Deadline First
Pessimistic
Optimized
Least Slack Time

## Slide 4: Related Works
Characteristics | [Tanase] | [Doerflinger et al. ] | [M. Vetromille et al.] | [Dannev & Platzner] | [Tang , Neil W.Bergmann] | This Work
Generalized Approach | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Vendor Independent | ✘ | ✘ | ✓ | ✓ | ✓ | ✓
Adaptability | ✘ | ✘ | ✘ | ✘ | ✘ | ✓
Scalability | ✘ | ✘ | ✓ | ✓ | ✘ | ✓
Fixed & Dynamic Priority | ✘ | ✘ | ✓ | ✘ | ✓ | ✓
Preemptive & Non-Preemptive | ✘ | ✘ | ✘ | ✘ | ✓ | ✓

## Slide 5: Communication Infrastructure
Figure 1 & 2.
Ariel Podlubne et al. “Model-Based Approach for Automatic Generation of Hardware Architectures for Robotics”

## Slide 6: Scheduler Design
States
Queue
Priority Computation
Fixed or dynamic
Preemption or Non-Preemption
Acc0
Acc2
Acc1
Acc3

## Slide 7: Pessimistic EDF State Machine
Init
WaitingRequests
SetGnt
WaitingNewRequests
UpdatePriorities
FindEarliest

## Slide 8: Homogeneous State Machine
Init
WaitingRequests
SetGnt
Sending

## Slide 9: Analysis and Evaluation
Scalability
  LUT
  FF
  Scaling Factor
Schedulability
  Accelarators served
  Length/Period ratio
  Latest Transmission
Performance
  Average Response Time
  Communication Channel Utilization
  Lateness
  Number of late Jobs
  Maximum Latency

## Slide 10: Scalability
Linear Scalability
Linear Scalability
 | Non-preemptive FP |  | Preemptive FP |  | Pessimistic EDF |  | Optimized EDF |  | LST | 
Average Scaling Factor | FF | LUT | FF | LUT | FF | LUT | FF | LUT | FF | LUT
 | 1.99 | 2.17 | 1.99 | 1.80 | 1.99 | 2.15 | 1.99 | 2.21 | 1.99 | 2.23

## Slide 11: Generated Values

## Slide 12: Schedulability
1/15
1/15
Length/Period ratio
Length/Period ratio
1/50
Length/Period ratio
1/100

## Slide 13: Performance
  Average Response Time
  Communication Channel Utilization
  Lateness
  Number of late Jobs
  Maximum Latency

## Slide 14: Average Response Times
Normalized horizontally.
Average response is larger with more accelerators.
More apparent in Fixed Priority Schedulers.
EDF and LST more apparent for 32 or more Accelerators.

## Slide 15: Completed Data Transmissions
Normalized vertically.
Emphasis on comparison of algorithms.
Pessimistic EDF least completed data transmissions.
Completed Transmission less for optimized EDF
and LST with more Accelerators.
Most data transmission for LST for 4 Accelerators
Preemptive fixed Priority for 8 Accelerators

## Slide 16: Lateness

## Slide 17: Optimized EDF vs LST
 | Optimized EDF |  | LST | 
Acc | LUT | FF | LUT | FF
2 | 265 | 205 | 333 | 335
4 | 736 | 405 | 1098 | 665
8 | 1853 | 803 | 2271 | 1327
16 | 3340 | 1601 | 4919 | 2643
32 | 7864 | 3185 | 8986 | 5264
64 | 15761 | 6379 | 20079 | 10553
128 | 32467 | 12756 | 40317 | 21017
256 | 6375 | 25390 | 81939 | 42034

## Slide 18: Data Channel Utilization
Pessimistic EDF Scheduler less than 50% for more than 8 Accelerators.
Only sends in one state
Optimized EDF slightly worse than the rest.
LST and Fixed Priorities more than 80%.

## Slide 19: Conclusions and Outlook
Generalizable, Feasible, Adaptable
Design Decisions effect on Performance
Schedulability differences between fixed and dynamic Priority implementations
Length/Period effect on Schedulability
Linear Scalability for resources for all algorithms
Consideration of resource utilization should accompany an increase in performance

## Slide 20: Bibliography
[1] Cristian Tanase. “Dynamic scheduler implementation used for load distribution between hardware accelerators (RTL) and software tasks (CPU) in heterogeneous systems”. In: The Journal of Supercomputing 76 (Dec. 2020).
DOI: 10.1007/s11227-020-03242-w.
[2] Alexander Doerflinger et al. “Hardware and Software Task Scheduling for ARM-FPGA Platforms”. In: Aug. 2018, pp. 66–73.
DOI: 10.1109/AHS.2018.8541481.
[3] M. Vetromille et al. “RTOS Scheduler Implementation in Hardware and Software for Real Time Applications”. In: Seventeenth IEEE International Workshop on Rapid System Prototyping (RSP’06). 2006, pp. 163–168.
DOI: 10.1109/RSP.2006.34.
[4] K. Danne and Marco Platzner. “Periodic real-time scheduling for FPGA computers”. In: June 2005, pp. 117–127. ISBN: 3-902463-03-1.
DOI: 10.1109/WISES.2005.1438720.
[5] Yi Tang and Neil W. Bergmann. “A Hardware Scheduler Based on Task Queues for FPGA-Based Embedded Real-Time Systems”. In: IEEE Transactions on Computers 64.5(2015), pp. 1254–1267.
DOI: 10.1109/TC.2014.2315637.
[6] Ariel Podlubne et al. “Model-Based Approach for Automatic Generation of Hardware Architectures for Robotics”. In: IEEE Access 9 (2021), pp. 140921–140937.
DOI: 10.1109/ACCESS.2021.3119061.

## Slide 21
Thank you for your attention!

## Slide 22: LUT and FF

## Slide 23
Accelerators
IPs to Com Interface

## Slide 25: Communication Infrastructure